## Slide 1: Overview of Spokane- Coeur d’Alene Hydrology
Dale R. Ralston PhD PE PG
Ralston Hydrologic Services, Inc.
Moscow, ID
October 28, 2015

## Slide 2: Topics for discussion
Coeur d’Alene Lake -- Inputs and outputs and what controls discharge and lake levels.
Spokane Valley – Rathdrum Prairie Aquifer – Relationship between the aquifer, the Spokane River and Coeur d’Alene Lake.
Ground-water/surface water relationships in basins other than the SVRP aquifer.

## Slide 3: Coeur d’Alene Lake

## Slide 4
USGS scientific investigations report 2009-5184

## Slide 5: Mean annual inputs to the lake based on 2000-2005 data
Coeur d’Alene River (near Harrison)
  1,475 square mile drainage
  41.0 percent of inflow to the lake
St. Joe River (near Chatcolet)
  1,720 square mile drainage
  49.5 percent of inflow to the lake
Creeks and ungaged tributaries
  555 square miles of drainage
  7.6 percent of inflow to the lake
Precipitation is 1.9 percent of inflow to the lake

## Slide 6: Mean annual outputs from the lake
Spokane River as measured at the Post Falls gage is about 94 percent of the outflow from the lake
Leakage from CdA Lake and the Spokane River above the Post Falls gage is about 4 percent of the outflow from the lake
Evaporation from the lake is about 1.4 percent of the outflow from the lake
Remainder is miscellaneous consumptive use of ground water and surface water

## Slide 7
Flow of glacial flood water from the north pushed the Spokane River to a location along the south side of the valley
Post Falls occurs because the river was superimposed over basement rock
Coeur d’Alene is a natural lake but the Post Falls Dam plays an important role in water management

## Slide 8
Operation of Post Falls Dam controls lake level and river discharge from late spring to early fall.
The river channel near the lake outlet controls lake level and river discharge at both extreme high lake stage and extreme low lake stage.
River channel from the lake outlet to Post Falls plays an important role in controlling lake level and river flow.

## Slide 9
Chart: Lake water level elevation in feet

## Slide 10
Hydrograph for Coeur d’Alene Lake for 2013
Approximate period when lake level is regulated by the Post Falls Dam
AVISTA – lake level held at 2,128 feet from as soon as possible in the summer to the Tuesday after Labor Day. Then, river flow is managed mostly for power production with a minimum discharge of 600/500 cfs (after 2009) until early winter when the dam no longer regulates flow.
Notes: The 2013 graph for lake water levels show that the lake level was held near 2,128 feet until late August.
AVISTA is required to hold the lake at about 2,128 feet starting as early as possible and continuing until the Tuesday after Labor Day each year.
Period of extreme low flow in the Spokane River at Spokane occurs in late August and early September.

## Slide 11
Hydrograph for the Spokane River near Post Falls, Idaho for 2013
Approximate period when lake level is regulated by the Post Falls Dam
Critical low flow period
Notes: Hydrograph for the river at Post Falls shows low flow in August with flow stepped up in early September as AVISTA lets more water past the Post Falls Dam.

## Slide 12: Spokane Valley – Rathdrum Prairie Aquifer and the Spokane River

## Slide 13
(From 2009 update of aquifer atlas)
(49%)
(59%)
Spokane River is the dominant recharge source and discharge area for the aquifer
(22 %)
(35%)

## Slide 14
Post Falls to Greenacres: Average river loss (aquifer recharge) was 388 cfs or 61% of the flow
R
Aquifer recharge from river loss during August 20-31, 2010 in the reach of the river from the Coeur d’Alene gage to the Greenacres gage
Coeur d’Alene to Post Falls: Average river loss (aquifer recharge) was 360 cfs or 36% of the flow
CdA gage (997 cfs)
Post Falls gage (637 cfs)
Greenacres gage (249 cfs)

## Slide 15
Greenacres gage (249 cfs)
Net river gain during August 20-31, 2010 in the reach of the river from the Greenacres gage to the Spokane gage
Spokane gage (917 cfs)
Greenacres to Spokane: Average net river gain (aquifer discharge) was 668 cfs

## Slide 16: Aquifer/river relationship relative to the state line
Most of the recharge to the aquifer occurs in Idaho
All of the aquifer discharge back to the Spokane River occurs in Washington
Much of the flow of the Spokane River is lost to the aquifer between the lake outlet and below Greenacres which is about six miles west of the state line.
Ground-water discharges back into the river starting below Greenacres; the flow of the river at the Spokane gage is greater than at the Post Falls gage.

## Slide 17
Upstream of this point the Spokane River is perched above the aquifer
Hydrogeologic Characteristics of the River/Aquifer system
Perched reach
Hydraulically
connected reach
From 2009 aquifer atlas
Spokane gage
Coeur d’Alene gage
Post Falls gage
Greenacres gage
SVRP Aquifer
Notes: Describe the river-aquifer system including the aquifer boundaries, the lakes and the river.
Point out that the river is perched above the aquifer from the lake to below Greenacres and cannot be impacted by GW pumping.
Identify the four gaging stations of importance.

## Slide 18
From USGS Circular 1376
Perched River – water table is below the bottom of the river channel – amount of aquifer recharge is controlled by the height of water in the river; it is independent of ground-water levels.
Losing River -- river is in hydraulic connection with the aquifer – amount of aquifer recharge from the river is controlled by the difference between the river water level and the ground-water level.
Gaining River – river is in hydraulic connection with the aquifer – amount of ground-water discharge to the river is controlled by the difference between the river water level and the ground-water level.

## Slide 19: Ground water pumping in Idaho cannot impact flow of the Spokane River in Idaho
Spokane River is perched above the aquifer within Idaho and about 6 miles west into Washington.
Ground-water pumping in Idaho cannot impact river flow in Idaho but can impact the flow of the river downstream of Greenacres in Washington.

## Slide 20: How has the river/aquifer system changed with development?
No pattern of long-term water-level decline in the aquifer
No significant change within the Coeur d’Alene Lake drainage; no reservoirs on St. Joe or CdA Rivers
Dam at Post Falls on the Spokane River controls lake level and flow only during the summer and fall.
No change to high and average annual flow in the river.
Seven-day low flow in the river has decreased with time.
Ground-water development in the SVRP aquifer is the most significant change to the water resource.
Notes: No impoundments within either the Coeur d’Alene or St. Joe River valleys.
Describe how AVISTA operates the Post Falls Dam.

## Slide 21
Wells located near Post Falls show that aquifer ground-water levels are currently at or above most of the 80-year period of record
Notes: Ground-water levels respond to changes in recharge quantities – but no pattern of long-term water level decline.
Ground-water levels in 2014 are higher than for most of the 80+ years of record.
A well near Rathdrum shows the same pattern.

## Slide 22: Ground Water and Surface Water in Areas other than the Spokane Valley – Rathdrum Prairie Aquifer

## Slide 23: Geology controls ground-water resources
Metamorphic rocks make up the ridges and mountains and yield very small quantities of water to wells.
The valleys are underlain by sediment and basalt with basalt providing the best aquifer for well development.
Distribution of metamorphic rocks create different ground-water basins
  Plummer area
  Tensed and the Hangman Creek Valley
  Worley and the Rock Creek drainage

## Slide 24
From Idaho Geological Survey website
Basalt
Sediment over basalt
Sediment
Metamorphic rock
Metamorphic rock
Metamorphic rock
Ground-water resources are very limited in areas underlain by metamorphic rock

## Slide 25
Basalt
Bedrock
Metamorphic rock
Metamorphic rock
From Idaho Geological Survey website
Metamorphic rock
Metamorphic rock
Plummer Area is surrounded by metamorphic rock

## Slide 26
Ground water and surface water in Basin 93 flows across the state line into Washington
Wells likely have little impact on the surface streams because of the geologic setting.

## Slide 27
The southern portion of basin 95 is tributary to Coeur d’Alene Lake
95
The amount of ground-water discharge to the lake is very small because of the geology of the area.

## Slide 28: Summary and Conclusions
Post Falls Dam only controls the level of Coeur d’Alene Lake and the discharge of the Spokane River during the period from early summer to late fall. The channel near the outlet of the lake controls lake level and river discharge during both high and low lake levels.
The Spokane River in Idaho is perched above the SVRP aquifer. Ground-water pumping from the aquifer cannot impact river flow within Idaho.
Complex geology controls ground-water in basins 93 and 95, likely with little connection to surface water.

## Slide 29: Thank you!!